## Slide 1
AGENDA
01 Technical — what goes wrong on board
02 Before you bunker — checks and approvals
03 Regulatory — IMO, EU and 2027
04 Commercial — premium and the PoS
Notes: Opening — 30 sec.
Biofuel is the one alternative fuel a customer can adopt without touching the ship. That is exactly why it gets underestimated.
Today: what actually goes wrong on board, what to check before bunkering, what the regulators require, and what the price really pays for.
Four parts, about 15 minutes. Source is the SSA Biofuels FAQ, August 2026 edition.

## Slide 2
Marine Biofuels — Five Things to Remember
01
Drop-in does not mean drop-and-forget
No engine conversion is needed — but tank, filter, purifier, temperature and material management all are.
02
Five technical risks, one endpoint
Water, oxidation, microbial growth, cold flow and the solvent effect all end in sludge — and then in blocked filters and purifiers.
03
The benefit comes from certification, not from the fuel
“We used biofuel” earns nothing. “We used certified sustainable biofuel” is what IMO and the EU recognise.
04
BDN + PoS are the two documents that matter
And from 1 January 2027 the IMO DCS conversion factor is calculated a different way.
05
The premium is compliance value, not just energy
Blends hold a structural premium over VLSFO because the buyers are owners with EU compliance exposure.
Source: Singapore Shipping Association, FAQ on Bunkering of Biofuels for Ocean-Going Vessels in the Port of Singapore, August 2026.
Notes: 1 min — say these five, then spend the rest of the deck backing them up.
Message 1 is the one customers most often miss. Drop-in means no engine conversion. It does not mean no management.
Message 3 and 4 are where the money is: the regulatory benefit comes from certification, not from the fuel itself.
Message 5 explains the price. The premium is not just energy — it is compliance value.

## Slide 3
Technical — How Biofuel Actually Fails on Board
One chain, three entry points
Biofuel
↓
Water / Oxidation / Microbial growth
↓
Degradation
↓
Sludge
↓
Filter & purifier problems
The FAME solvent property adds a second source. Biofuel dissolves the sludge and deposits already sitting in the tank, so filters can clog heavily in the first days after a switch — from old dirt, not from the new fuel.
Manage it in this order
1. Tank cleaning
↓
2. Bunkering
↓
3. Filter monitoring
↓
4. Fuel analysis
Clean the tank before the first biofuel stem — not after the first filter alarm.
Flush the system and watch filters closely through the changeover period; the rate settles once the old deposits have been carried out.
Notes: 2 min — the single most useful slide for a chief engineer.
Read the chain on the left out loud. Water, oxidation and microbial activity all end in the same place: sludge, and then blocked filters and purifiers.
The FAME solvent property is the one that surprises crews. The fuel does not create the deposit — it releases what was already on the tank walls. So the clogging is worst right after switching, then settles.
That is why the sequence on the right matters. Clean the tank first, and watch the filters hardest in the first days after bunkering.

## Slide 4
Additives — One Problem, One Additive
What each additive is for
Problem
Additive
Water in the fuel
Demulsifier — helps water separate out
Microbial growth
Biocide — inhibits bacteria and fungi
Oxidation
Antioxidant — interrupts the oxidation chain
Corrosion
Corrosion inhibitor
Biofuels are hygroscopic — they absorb water from the air. Leaking heating coils, venting and condensation in the tank headspace all add to it.
Dosage and efficacy should be agreed between supplier and end user — not decided on board.
What additives cannot do
Oxidation is irreversible. Once it has happened, an antioxidant cannot restore the fuel to its original condition — it can only slow further deterioration.
So an antioxidant is a shelf-life measure, taken before storage. It is not a remedy for fuel that has already degraded.
Water is the multiplier. It feeds microbial growth, drives hydrolysis, and accelerates oxidation — remove it first and the other additives work less hard.
Order of defence: keep water out, then dose — not the other way round.
Notes: 1 min — keep it short, it is a reference slide.
One additive per problem. Nothing here is a general-purpose fix.
The line to emphasise is the antioxidant caveat: oxidation is irreversible. An antioxidant slows what has not happened yet. It does not restore fuel that has already degraded.
And the FAQ is explicit that dosage and efficacy should be agreed between supplier and end user — not decided on board.

## Slide 5
Storage — Three Rules Worth Remembering
The three rules
1
Keep the fuel about 10 °C above the pour point on the Certificate of Quality
2
Avoid temperature swings
3
Use it within about three months
If the temperature has dropped below the pour point, heat the fuel until all waxes redissolve. Pour point can understate waxing — use Wax Appearance Temperature where it matters.
Three months is a practical rule of thumb, not a hard quality limit. GCMD stored B24 on board for six months and the acid value stayed within ISO 8217 limits.
Monitor these four during long storage
Indicator
What it tells you
Oxidation stability
The most direct sign of degradation
FAME content
Falls as esters break down, or on dilution
Acid value
Rises as free fatty acids form
Water content
Rises with absorption, and accelerates oxidation
If degradation is mild the fuel can often still be used — raising filtration temperature, reducing flow rates, in-line blending with fresh bunkers. Consult Class or the testing laboratory before deciding.
Fresh in, fresh out.
Notes: 1 min 30.
Three rules. Ten degrees above pour point, no temperature swings, use it within about three months.
Be honest about the three months. GCMD stored B24 on board for six months and the acid value rose but stayed inside ISO 8217 limits under the conditions tested. So three months is a practical rule of thumb, not a cliff.
If a customer has to store longer, the answer is not to refuse — it is to monitor the four indicators on the right and keep the stock turning.

## Slide 6
Two Things That Get Misread
B30 is not 30% FAME
The number after the B is the bio-content by volume — not the FAME content. The actual FAME share depends on the bio-component used.
EN 14214 compliant B100
FAME ≥ 96.5% by mass
B30 blend
30% × 96.5% ≈ 28.95% FAME
It matters whenever anyone calculates a blend ratio or an emission factor.
Approving the engine is not approving the ship
Everything in the fuel path has to be confirmed as suitable for the specified blend. Any one of these can be the weak link:
Engine
Purifier
Filter
Fuel treatment plant
Boiler
Seals and gaskets
Fuel tank and piping
Coatings and materials
FAME attacks rubber. Joints, seals and gaskets need checking before the first stem.
Notes: 1 min — two corrections customers appreciate.
First, B30 is not 30 percent FAME. The number is bio-content by volume. Since EN 14214 B100 is at least 96.5 percent FAME by mass, B30 gives you about 28.95 percent. It matters when anyone calculates blends or emission factors.
Second, checking the engine is not checking the ship. Purifiers, filters, the treatment plant, the boiler, seals and gaskets, and the tank and piping all sit in the fuel path. Any one of them can be the weak link.

## Slide 7
OEM Confirmation and What Class Asks For
Get it in writing
Consult the engine maker before the first biofuel stem and obtain written confirmation — a service letter, a biofuel specification, or a Letter of No Objection — stating which blends the engine accepts.
Some engines also require a different lubricating oil on biofuel. Ask.
If the OEM will not confirm, Class will assess the installed arrangement and any proposed modification instead.
And do not skip the crew
Familiarisation and training are essential, and standard operating procedures usually need modifying before the first stem.
Typical Class submission pack
01
Ship particulars and the engines and machinery involved
02
Biofuel specifications, MSDS and analyses
03
Proposed modifications to storage, fuel systems and equipment
04
Fuel service tank arrangement
05
Fuel system material and coating specifications
06
OEM specifications, agreements and correspondence
07
Ship implementation plan and associated assessments
08
MARPOL compliance details and any long-term testing plan
Class can also handle the Flag Administration application as a recognised organisation.
Notes: 1 min 30.
Get the confirmation in writing. A Letter of No Objection, or a service letter, stating which blends the engine accepts. Verbal assurance is not enough if a claim follows.
If the OEM will not confirm, it is not a dead end — Class will assess the installed arrangement and any proposed modification instead.
The right-hand list is what Class typically asks for. Worth sending to the customer early, because assembling it takes longer than they expect.

## Slide 8
Regulatory — What IMO and the EU Each Ask
IMO — DCS, CII and the conversion factor
Requirement
Threshold
WtW GHG reduction
at least 65% vs fossil MGO
Fossil MGO reference
94 gCO₂eq/MJ
So the biofuel must reach
33 gCO₂eq/MJ or below
Certification scheme
ISCC or RSB (CORSIA-approved)
Documents
PoS issued with the BDN
The conversion factor is the certified WtW GHG figure multiplied by the lower calorific value, and it can never be less than zero. A lower factor feeds through to a better CII rating.
EU — two regulations, two questions
Regulation
The question it asks
EU ETS
“How much did the ship actually emit?” → Tank-to-Wake
FuelEU Maritime
“What is the lifecycle GHG intensity of the energy used?” → Well-to-Wake
FuelEU is not a cap-and-trade scheme and not a tax. It sets GHG intensity limits and penalises ships that exceed them, to level the field between cheap fossil fuel and more expensive low-carbon alternatives.
Not every biofuel qualifies. Miss the RED III 65% saving, or use a food or feed crop feedstock, and it counts as its fossil equivalent.
Notes: 2 min — the part customers ask about most.
IMO first. Interim guidance recognises certified sustainable biofuel: at least 65 percent well-to-wake reduction against fossil MGO at 94 grams, so 33 grams or below. Certified under ISCC or RSB. And the Proof of Sustainability has to come with the Bunker Delivery Note, or none of it counts.
EU next, and the easy way to remember it: ETS asks what the ship actually emitted — tank-to-wake. FuelEU asks what the energy cost over its whole life — well-to-wake.
The key point for both: not every biofuel qualifies. Miss the RED III 65 percent threshold, or use a food or feed crop feedstock, and it is treated as its fossil equivalent.

## Slide 9
The 2027 Change to Watch — MEPC.1/Circ.905 Rev.1
What changes on 1 January 2027
Conversion factor for a blend
Until 2026
Energy-weighted average of the components
From 2027
Mass-weighted average of the components
And if the biogenic component is not certified, the blend is treated as the equivalent fossil fuel type.
The revised guidance was approved at MEPC 84 in April 2026 and applies from 1 January 2027, to line up with the start of the next DCS data collection period.
What it means in practice
01
Same fuel, different number — and it feeds straight into CII
02
SEEMP Part II and Part III need updating, and DCS reporting with them
03
An uncertified stem earns no credit at all, however green the feedstock
04
So the PoS has to be chased at purchase, not at reporting time
Buying biofuel is not the compliance event. Certification and the PoS are.
Notes: 1 min 30 — flag this as the change to plan for.
From 1 January 2027, the conversion factor for a blend moves from an energy-weighted average to a mass-weighted average. Same fuel, different number, and it feeds straight into CII.
The second change is the one with commercial teeth: if the biogenic component is not certified, the whole blend is treated as the equivalent fossil fuel.
So the message to the customer is simple. Buying biofuel is not the compliance event. Certification and the PoS are.

## Slide 10
Quality and Testing — What to Look For
The main risk chain
Oxidation
↓
Degradation / acid formation
↓
Sludge / sediment
↓
Filter & purifier blockage
Three side paths into the same place
Water
→ microbial growth → sludge
Low temperature
→ wax → gelling
FAME solvent property
→ material compatibility
Which standards to test against
Standard
Role
ISO 8217:2024
The base specification for marine fuels
TR 140:2025
Additional parameters for marine biofuel blends
EN 14214 / ASTM D6751
The FAME component (sulphur, cloud point and CFPP aside)
And one test worth adding
Iodine value measures unsaturation — the double bonds in the fatty acid chains. More unsaturation means faster oxidation, more polymerisation into gums and sediments, and poorer storage stability.
It is the cheapest early warning available on a bio blend.
Notes: 1 min 30.
The main chain runs oxidation, degradation and acid formation, sludge, then blockage. Three side paths feed into it: water leading to microbial growth, low temperature leading to wax, and the FAME solvent property attacking materials.
On testing, ISO 8217:2024 is the base but it is not sufficient on its own — TR 140:2025 adds the parameters that matter for a blend.
Iodine value is worth calling out. It measures unsaturation, and unsaturation drives oxidation, polymerisation and sediment. It is the cheapest early warning you can buy.

## Slide 11
Commercial — The Premium and the PoS
Pricing through 2024–25
Measure
Level
B24 / B30 premium over cargo prices
low to mid USD 200/t
Where it held firmest
Singapore
What blend prices track
Crude and VLSFO, not bio fundamentals
The premium held because the buyers were owners with EU compliance exposure. Purchasing was driven by regulatory need rather than arbitrage, so suppliers kept delivered premiums even when bunker demand softened.
Corrections showed up as narrower premiums, not as falling prices.
The PoS does not arrive with the BDN
Point
What to expect
Issued on delivery?
No — the BDN is, the PoS is not
Typical lead time
about 30 days for a new batch
Repeat lifts
Faster, from the same feedstock batch
One delivery
Can carry more than one PoS
The supplier has to calculate the quantity allocation across the chain, and internal compliance checks, approval steps and any traders in between all add time. Quantity is normally allocated against the BDN figure.
Set this expectation before the first stem.
Notes: 1 min 30.
Through 2024 and 2025 the B24 and B30 premium held in the low to mid 200 dollars per tonne over cargo prices, mainly in Singapore.
It held because the buyers were owners with EU compliance exposure. When demand softened the premium narrowed, but prices did not fall — they track crude and VLSFO, not biofuel fundamentals.
Then the PoS. Unlike the BDN it is not issued on delivery, because the supplier has to allocate quantity across the chain. Around 30 days for a new feedstock batch, faster afterwards, and one delivery can carry several PoS. Tell customers this up front — it is a common source of complaints.

## Slide 12
One Chain — Technical, Regulatory, Commercial
TECHNICAL
REGULATORY
COMMERCIAL
Manage water, oxidation, microbial growth, cold flow and the solvent effect — and the machinery stays protected.
Certify the fuel and secure the PoS — and the fuel converts into a recognised GHG benefit under IMO and the EU.
That benefit is what the premium is actually buying — compliance value, not just energy content.
Protects the ship
Earns the credit
Justifies the price
Break any one link and the customer pays a USD 200 premium for a fuel that earns no compliance credit — and still has a filter problem.
Source: Singapore Shipping Association, FAQ on Bunkering of Biofuels for Ocean-Going Vessels in the Port of Singapore, August 2026 (3rd edition). Referenced standards: ISO 8217:2024, TR 140:2025, MEPC.1/Circ.905 and Rev.1.
Notes: 1 min — close on the chain, then invite questions.
This is the line to leave them with. The technical work protects the machinery. The certification converts the fuel into a regulatory benefit. And that benefit is what the premium is actually buying.
Break any one link and the customer is paying a 200 dollar premium for a fuel that gives them no compliance credit and a filter problem.
That is where we can help — on all three links, not just the supply.