## Slide 1
Lubrication Strategy Follows Criticality
Classified as Internal - This content is proprietary information intended for employees and partners only.
Why lubrication is preventive maintenance
If roughly 80% of failures trace back to contaminated or degraded oil, then every lubrication action counts as preventive maintenance — not housekeeping.
The same logic as heart health: diet and a blood test every six months cost very little. Surgery does not.
The six functions of a lubricant
Reduce friction
Reduce wear
Prevent corrosion
Remove heat
Remove contaminants
Transmit fluid power
There is no single right answer — spend where it counts
Equipment character
What to specify
Cheap, easy to replace, not critical
A basic lubricant is enough
Spare held on board, quick swap
Standard grade
Stern tube, thruster — costly, hard to reach, expensive downtime
Specify the best available
Criticality — not price — sets the specification.

## Slide 2
Friction and the Four Lubrication Regimes
Classified as Internal - This content is proprietary information intended for employees and partners only.
Stribeck curve
Friction against ZN/P, and where each regime shows up on board
Slow and heavily loaded → higher viscosity, so the film forms sooner.
The intuition
Push a block across concrete and friction is highest before it moves — and barely depends on speed.
Add a lubricant and friction drops sharply. Keep raising the speed and it climbs again, the way a ship has to push aside more water the faster it goes: now the oil itself is what must be sheared.

## Slide 3
Base Oils — Mineral and Synthetic
Classified as Internal - This content is proprietary information intended for employees and partners only.
Two ways to make a base oil
Mineral — refined from crude oil. A box of mixed Lego: many shapes, many sizes, whatever the barrel gave you.
Synthetic — known molecules assembled into the structure you actually want.
API base oil groups
Group III is sold as synthetic in most markets, but it is still refined mineral stock — synthetic in name.
Group IV (PAO) is the workhorse synthetic — gears and some compressors.
Group V is everything that fits nowhere else, which does not make it better.
Viscosity Index = how much the oil thins as it heats. Higher VI, flatter response.

## Slide 4
Additives, Viscosity and Grease
Classified as Internal - This content is proprietary information intended for employees and partners only.
Additive families
Additives are the most expensive part of the blend — do not pay for what the application does not need.
Open to atmosphere
More oxidation inhibitor
Heavily loaded
Extreme pressure (EP)
Hydraulic pump
Antiwear (AW)
Compressor, turbine
R&O — rust and oxidation
The three properties that matter most
1
Viscosity
2
Viscosity against temperature
3
Viscosity against pressure
Kinematic viscosity is the figure normally quoted; ISO VG is the grading standard.
Grease = base oil + thickener + additives
Think of a sponge holding water. Squeeze it and water comes out; release it and the sponge takes the water back.
The thickener matrix holds the base oil until the bearing turns and load comes on. The oil is pushed out, and it is the base oil that does the lubricating.
Consistency is graded by worked penetration (NLGI). NLGI 2 is the general multipurpose grade.